## Slide 1
Rules:
„Centerline and Laneboundary point sequences are in the same direction along the direction of the road (e.g. along „s“ in OpenDRIVE)“
„For Roads, the Successor and Antecessor refer to the direction of the point sequences“
„If the „centerline-is-driving-direction“-flag is different on the successor lane compared to the current lane a vehicle is driving on, means that the point sequence on the next lane will be followed in opposing direction“
„If two lanes are completely connected with each other the successor and antecessor IDs are the same“
„For Intersections, the Successor and Antecessor refer to the possible connections across the intersection“
=> Antecessor/Successor assignment is different on „road“-lanes and on „intersection“-lanes

## Slide 2
Road-Road Connections (end+start connected)
L1
L2
true
false
s
flag: „centerline-is-driving-direction“
Road1
L4
L3
true
false
s
Road2
+
Lane | Antecessor | Successor
L1 | … | L4
L2 | … | L3
L3 | L2 | …
L4 | L1 | …

## Slide 3
Road-Road Connections (end+end connected)
L1
L2
true
false
s
Road1
L4
L3
false
true
s
Road2
+
Lane | Antecessor | Successor
L1 | … | L4
L2 | … | L3
L3 | … | L2
L4 | … | L1
flag: „centerline-is-driving-direction“
Example: On L1 the vehicle follows the centerline points in ascending order. Since the „centerline-is-driving-direction“-flag is different on the successing lane, the vehicle has to follow the centerline points on L4 in descending order.

## Slide 4
L1
s
L2
s
true
true
Lane | Antecessor | Successor
L1 | L2 | L2
L2 | L1 | L1

## Slide 5
L1
L2
L3
L4
true
false
false
true
L5
L6
true
false
Lane | Antecessor | Successor
L7 | L1 | L5
 | L1 | L3
 | L6 | L3
 | L6 | L2
 | L4 | L2
 | L4 | L5
L7

## Slide 6
L1
L2
L3
L4
true
false
false
true
L5
L6
true
false
L7
Lane | Antecessor | Successor
L7 | L1 | L5
 | L1 | L3
 | L6 | L3
 | L6 | L2
 | L4 | L2
 | L4 | L5
Example: Vehicle drives L1, L7, L5
On L1:
driving along centerline in descending order
Since „centerline-is-drv-dir“ == false => proceed to antecessor (L7)
L7 holds L3 and L5 as possible sucessors from antecessor L1
Example: Vehicle drives L6, L7, L2
On L6:
driving along centerline in ascending order
Since „centerline-is-drv-dir“ == true => proceed to successor (L7)
L7 holds L3 and L2 as possible sucessors from antecessor L6